## Slide 1: Function Blocks of OWCI Software
General Setting
  Hardware control, include pilot width and device address.
Test Mode
  Enter Test Mode, supporting different DUTs.
Registers Read/Write
  Single or burst registers read or write.
OTP Window
  OTP operation, bit by bit or byte by byte, load data from a .txt file and save data to a .txt file.
Script Window
  Load script from a .txt file and execute, edit a script and execute or save to .txt file.
Fuse
  Support eFuse.
Operation log
  Display all the operations include commands and return data

## Slide 2: Over View of OWCI Software

## Slide 3: Blocks Review 1
General Setting,
Test Mode,
Registers Read/Write,
Fuse.
  These operations are almost the same as last version software.

## Slide 4: Blocks Review 2
Functions of OTP Window
  Edit the window directly, supporting edit bit by bit or byte by byte, and blow OTP;
  Save window data to a .txt file as right format;
  Load data form a .txt file as right format, and blow OTP;
  After load, also can edit the updated window, and then save to a file or blow OTP;
  Command line supporting, ext. writeotp.exe OTP Demo.txt blowotp.exe OTP Demo.txt (Note: xxxxotp.exe and OTP Demo.txt must be in same directory).
OTP setting name

## Slide 5: Blocks Review 3
Functions of Script Window
  Edit a new script, and execute;
  Edit a new script, and save to a .txt file as right format;
  Load script form a .txt file as right format, and execute;
  After load script, also can edit in the updated window, and then choose to save to a new file or execute.
  Command line supporting, ext. execute.exe Script Demo.txt (Note: xxxxotp.exe and OTP Demo.txt must be in same directory).
!!! Each command in single line
Script name
Command

## Slide 6: Supporting Commands
Write: Addr 0x80; Data 0x10
Read: Addr 0x80
BurstWrite: Addr 0x80; Num 0x10; Data 0x00
BurstRead: Addr 0x80; Num 0x10
SetPilot: 200us
SetDelay: 100ms
Fuse: 160ns; 10ms
WriteOTP:
ReadOTP:
BlowOTP:
SetLRasOwci:
SetConfigasOwci: