## Slide 1: Description of Commands 1
WRITE: 0x80: 0x10; //write value 0x10 to register 0x80
READ: 0x80; //Read value of register 0x80
BURSTWRITE: 0x80; 0x02: 0x03 : 0xAA; //Burst write 0x03 and 0xAA to register 0x80 and 0x8A
BURSTREAD: 0x80: 0x10; //Burst Read values of register 0x80-0x90
SETPILOT: 200us //Set pilot as 200us
DELAY: 100ms //Delay 100ms
FUSE: 160ns; 10ms //Set fuse pulse as 160ns, fuse clock duration as 10ms, and fuse
WRITEOTP: //Write OTP data to relative registers
READOTP: //Read OTP data
BLOWOTP: //Blow OTP, take care of POWER
SETLRASOWCI: //Set LR pin on PCB as OWCI pin
SETCONFIGASOWCI: // Set CONFIG pin on PCB as OWCI pin

## Slide 2: Description of Commands 2
WR
SWR
WREG
WRITE
WRITEREG
WRITEREGISTER
Write Single Register
RR
RD
SRD
RREG
READREG
READ READREGISTER
Read Single Register
BWR
BURSTWRITE BURSTWRITEREG BURSTWRITEREGISTER
Burst
Write Registers
BRR
BRD
BURSTREAD
BURSTREADREG
BURSTREADREGISTER
Fuse
FUSE
Burst
Read Registers
Set delay time
SETDELAY
SD
DELAY
Set pilot width
SETPILOT
SP
Set pilot width
SETPILOT
SP
Set LR as OWCI
SETLRASOWCI
SLAO
Set CONFIG as OWCI
SETCONFIGASOWCI
SCAO
Write OTP
WRITEOTP
WROTP
Read OTP
READOTP
RDOTP
Blow OTP
BLOWOTP
BOTP