## Slide 1: Overview of OWCI Software

## Slide 2: Function Blocks of OWCI Software
General Setting
  Hardware control, include pilot width and device address.
Test Mode
  Enter Test Mode, supporting different DUTs.
Registers Read/Write
  Single or burst registers read or write.
Fuse
  Support eFuse.
OTP Window
  OTP operation, bit by bit or byte by byte, load data from a .txt file and save data to a .txt file.
Script Window
  Load script from a .txt file and execute, edit a script and execute or save to .txt file.
Operation log
  Display all the operations include commands and return data
  These operations are almost the same as last version software.

## Slide 3: New Features
OTP window
  Advantages:
    1. Totally new designed tools for eMemery operation in md008, could be re-used in future project as well;
    2. For each project, software will initialize OTP window based on a default config file, no need to rebuild a new GUI.
Script window
  Advantages:
    1. Script operation is a simple, flexible and efficient way for both PE and designers to do validation;
    2. For each project, no need to rebuild a new GUI, just write new script and execute;
    3. Script file is easy save and re-used between different sites.

## Slide 4: Blocks Review – OTP window
Functions of OTP Window
  Edit the window directly, supporting edit bit by bit or byte by byte, and write OTP or blow OTP;
  Save window data to a .txt file as right format;
  Load data form a .txt file as right format, and write OTP or blow OTP;
  After load, also can edit the updated window, and then save to a file, write OTP or blow OTP;
  Command line supporting, ext. writeotp.exe OTP Demo.txt blowotp.exe OTP Demo.txt (Note: xxxxotp.exe and OTP Demo.txt must be in same directory).
OTP setting file
OTP Window
OTP setting name

## Slide 5: Blocks Review – Script window
Functions of Script Window
  Edit a new script, and execute;
  Edit a new script, and save to a .txt file as right format;
  Load script form a .txt file as right format, and execute;
  After load script, also can edit in the updated window, and then choose to save to a new file or execute.
  Command line supporting, ext. execute.exe Script Demo.txt (Note: xxxxotp.exe and OTP Demo.txt must be in same directory).
!!! Each command in single line
Script file
Commands
Script name
execute from line3 to line 29

## Slide 6: Description of Commands 1
WRITE: 0x80: 0x10; //write value 0x10 to register 0x80
READ: 0x80; //Read value of register 0x80
BURSTWRITE: 0x80; 0x02: 0x03 : 0xAA; //Burst write 0x03 and 0xAA to register 0x80 and 0x8A
BURSTREAD: 0x80: 0x10; //Burst Read values of register 0x80-0x90
SETPILOT: 200us //Set pilot as 200us
DELAY: 100ms //Delay 100ms
FUSE: 160ns; 10ms //Set fuse pulse as 160ns, fuse clock duration as 10ms, and fuse
WRITEOTP: //Write OTP data to relative registers
READOTP: //Read OTP data
BLOWOTP: //Blow OTP, take care of POWER
SETLRASOWCI: //Set LR pin on PCB as OWCI pin
SETCONFIGASOWCI: // Set CONFIG pin on PCB as OWCI pin

## Slide 7: Description of Commands 2
WR
SWR
WREG
WRITE
WRITEREG
WRITEREGISTER
Write Single Register
RR
RD
SRD
RREG
READREG
READ READREGISTER
Read Single Register
BWR
BURSTWRITE BURSTWRITEREG BURSTWRITEREGISTER
Burst
Write Registers
BRR
BRD
BURSTREAD
BURSTREADREG
BURSTREADREGISTER
Fuse
FUSE
Burst
Read Registers
Set delay time
SETDELAY
SD
DELAY
Set pilot width
SETPILOT
SP
Set pilot width
SETPILOT
SP
Set LR as OWCI
SETLRASOWCI
SLAO
Set CONFIG as OWCI
SETCONFIGASOWCI
SCAO
Write OTP
WRITEOTP
WROTP
Read OTP
READOTP
RDOTP
Blow OTP
BLOWOTP
BOTP